## Slide 1: Embedded Track #1
Rules of the Game

## Slide 2: Production costs
Production costs is the sum of development costs plus the cost of production.
  The development costs is sometimes called the non recurring costs.
  Recurring Costs/Unit is the ( recurring cost)/(number of units)
  Number of IOT systems we are producing maybe on the order of 10’s.
For example, if a board layout cost are $1000 dollars, then the recurring cost for the board for a unit of 10 unit is $100.00.
  This does not include populating the board
  This does not include the costs of the pc board or the costs of the parts
  The costs of parts can be 3X the cost of a large volume producer
    One of the reason low volume systems in America are made in China
  Also, the hardware costs have to multiplied by 3X to a customer for sustainable environment.
  This means that we could be at a 9x cost advantage to a large manufacturer
Conclusion
  We cannot do things the conventional way
  Many of my lost friends have not made the transition

## Slide 3: Hacking won’t work either
Hacking can produce a single unit but with problems.
  Lots of jumper wires
  Lots of manual labor
  Lots of debugging to get it to work
  In essence not very reproduceable

## Slide 4: What are the solutions?
We need to be able to produce 100 units.
After 100 units, capital can be raised to redesign the unit to lower costs and reduce assembly costs.
Requirements
  Need to assemble 100 units in a garage.
  Minimal Capital Equipment
    Laptop
    Voltmeter
    Low cost soldering station
    Low cost test setups
    Misc mechanical tools
  Need Skilled Assemblers and Technicians

## Slide 5: SCADA, (PLC) is one Solution Raspberry PI is controller to PLC
SCADA solution requires little hardware NRE.
Low cost SCADA equipment can be purchased at
  www.automationdirect.com
SCADA equipment is usually FCC and UL approved.
Low cost plc’s are price competitive
Terminal Blocks and other wiring solutions are available to handle the wiring complexity
If we are dealing with greater than 48 volts, this may be the only solution.
My farm irrigation system is based upon a SCADA type solution.
  Took me several years to realize this.

## Slide 6: Example of a SCADA Soluton 6 reasons why automation improves beer making Application Update: A beer equipment manufacturer uses off-the-shelf automation components to build affordable equipment and systems for craft brewers. https://www.controleng.com/single-article/6-reasons-why-automation-improves-beer-making/d5a166a19d45cecd32e49a4f1c36f13c.html
$80 dollar PLC
Expansion Modules ~ $50 Each

## Slide 7: Essence of Solution
Low Cost
PLC’s
Proprietary
SCADA
Serial Modbus
Mobile Phone
Tablets
WIFI

## Slide 8: My Solution that I used on my farm
Cloud Services
Open Source
Nano Data Center
Open Source
Low Cost PLC and other devices
Serial Modbus

## Slide 9: Need to make a scaled down PLC Cabinet
I start with $40 r
Outdoor load center
From home depot
Remove the insides

## Slide 10: Use DIN Rails to add components
IOT Edge
Device
Field
Remote
Unit
Wiring will
Be improved
On next generation

## Slide 11: Field Remote unit deployed
Picture of Remote
Deployed
Units
Sprinkler
Wire
Provides
The power
And RS485
Links to Units

## Slide 12: Remote Units serviced several years Including this

## Slide 13: What about other approaches
The SCADA approach is effective for switching relays and discrete I/O.
SCADA approach has limitations.
  Limited Analog Processing
  Analog Capability is expensive.
    PLC’s go from $80 to $200 range.
  I2C and SPI devices are required.
We need to produce modules and wiring solutions which are reproduceable and reasonably cheap.

## Slide 14: Rule #1 3X Markup
Do not apply the 3X Markup to hardware items that are purchased.
  Many companies collapsed under that rule.
Corollary
  Only develop what is required.
Use Bread Board Approach

## Slide 15: Bread Board Approach First Step: Prototype on Solderless Prototyping Boards
If the circuits will not fit on a bread board, break system out into smaller slaves

## Slide 16: Cannot Deploy Solderless Will not hold connectors
3 boards for $14.00

## Slide 17: Criteria for selecting processors
Processors which we use must be prototyping boards
  Cannot afford to construct a custom board
Prototype processor boards must fit into prototyping boards.
Two such processors are shown in the next pages/

## Slide 18: PCB boards can be produced with vendor supplied tools.
ExpressPCB offers 4 layer boards 3.8”X2.5” for $30.00

## Slide 19: PSOC 4
The PSOC 4 is less than $5.00 from arrow ( orders over $20.00 ship overnight free)
For units over 1000 the price is $3.50 from Cypress.
Free Development tools from cypress.

## Slide 20: PSOC 5
This part has 4 instrumentation amplifiers and a high resolution a/d up to 18 bits. Also, the part has 4 DACS. Use this part when instrumentation situations arise.
The price of the part is $15.00 from Digi Key and $9.20 from Arrow.

## Slide 21: Connections
Prototyping
Bread Board
PSOC
Module
IOT
Controller
I2c
Connectors

## Slide 22: Unique Abilities of PSOC Modules
The I/O within reason can be programmed to different pin types.
It is possible to have the same board be configured to do many roles.
Makes it easier to develop a pcb for low volume applications.

## Slide 23: Extending Range of I2C
Allows Bus Capacitance of 400 pF on Main I2C Bus (Sx/Sy Side) and 3000 pF on Transmission Side (Lx/Ly Side)
Dual Bidirectional Unity-Voltage-Gain Buffer With No External Directional Control Required
Drives 10× Lower-Impedance Bus Wiring for Improved Noise Immunity
Multi-Drop Distribution of I2C Signals Using Low-Cost Twisted-Pair Cables
I2C Bus Operation Over 50 Meters of Twisted-Pair Wire

## Slide 24: Other approaches?
Other approaches are welcome.
Solution to this problem is critical to the success of deploying complex IOT systems.