## Slide 1: PLC Irrigation Controller

## Slide 2: PLC Irrigation Controller Description
The Irrigation Controller is my basic field irrigation controller.
  22 Irrigation Controllers
  (8) 24 Volt Digital Inputs
  The first 4 digital inputs can be used as flow meter counters
  The field installation is designed to be done without opening the enclosure.
Automation Direct C0-00DR-D plc
  User Manual
    https://cdn.automationdirect.com/static/manuals/c0userm/c0userm.html

## Slide 3: Field Connection
The PLC controller will have three wire bundles
  7 Wire Bundle containing control and power signals
  12 Wire Bundle containing sprinkler inputs 1-11 + common return
  12 Wire Bundle containing sprinkler inputs 12-22 + common return

## Slide 4: Power and Control Bundle
The power and control Bundle contains the following lines
  Blue – 24 volts
  White --24 return
  Yellow --Sprinkler Power High
  Green – Sprinkler Power Low
  Red – RS485 High
  Orange – RS485 Low
  Black or Brown 485 Ground

## Slide 5: Connection – Match Colors of Controller Box with Field Cable
Sprinkler
Wire
Provides
The power
And RS485
Links to Units

## Slide 6: Sprinkler Cables
The sprinkler inputs are referenced by cable connector, connector 1 (1-11) and connector 2 (12-22)
The white wire in the cable is the sprinkler power return. The next wire after the white wire is either sprinkler #1 or #22.
Inputs Numbers can be determined based upon counting from the white wire

## Slide 7: Irrigation Controller Design
Enclosure Design is described in Appendix A
24 Volt inputs are designed in Appendix B
Relay Drive capability is described in Appendix C
Wiring Consideration is described in Appendix D
RS485 Implementation is described in Appendix E
Lightning Protection Appendix F

## Slide 8: Appendix A Enclosure Design
Outdoor Electrical Load Center Boxes are used as shown below.
The Insides of the Load Center Box is removed

## Slide 9: Enclosure Design Continued
A 10- 15 degree lower temperature in summer is possible if the enclosure is painted white.

## Slide 10: Enclosure Design has proven resilient
The Enclosure Design has been used for over 4 years. And survived a snow storm

## Slide 11: Enclosure Design Continued
Attached Two DIN Rails as shown in the picture below. Exact position of the DIN Rails is dependent upon the enclosure selected.

## Slide 12: Enclosure Design Continued
Punch out three ½ cable conduits and attach cable retainers.
The first punch out cable is 7 strand 18 gauge sprinkler wire.
The second and third punch out cable is 13 strand 18 gauge sprinkler wire.

## Slide 13: Populate Components on Din Rail
Din Rail in Middle
3 unit Plc
Diode Terminal Block 1-11
Din Rail at Top
8 input blocks + ground terminal
Diode Terminal Block 12-22

## Slide 14: Appendix B PLC Input Design
1. Recommended Layout for PLC Inputs
2. Actual Input Implementation
3. PLC Inputs are configured as sourcing
4. Performance Of PLC opto isolators
  Impacts Voltage Threshold
  Impacts Flow Meter Maximum Count

## Slide 15: Ideal Arrangement For Inputs

## Slide 16: Actual Implementation for Inputs Extra 24 volt power supply would take an Extra Two Wires

## Slide 17: Wiring of The PLC Inputs. Devices pull to ground

## Slide 18: Catches pulses on order of 10000 Hz opto isolators limit

## Slide 19: Appendix C Relay Drive Considerations

## Slide 20: Relay Output Considerations
The Circuit for the PLC Relay Drive is shown below. The strength of the transorb is 20 J. Automation Direct recommends
  Additional transient suppression should be used in both these examples. If you are unable to measure the transients generated by the connected loads of your control system, using additional transient suppression on all inductive loads would be the safest practice.

## Slide 21: To Add Additional Relay Protection The following Terminal Block was added

## Slide 22: Wiring Considerations
In the field the sprinkler wire is 18 gauge
  The current caring capacity is 2.3 amps
A solenoid short will cause 4 amps to flow through the system for as much as 15 seconds.
11 wires needed to be color coding
The wiring for the sprinkler lines inside the chasis was selected as 18 gauge wire.
Current Carring Capacity for various wire sizes can be found at
  https://www.powerstream.com/Wire_Size.htm

## Slide 23: Appendix E RS-485 Considerations
Will be describe next week

## Slide 24: Appendix F. Lighting Considerations
A 1N6284A transorb placed across the 24 volt power lines.
  The transorb will ingage if the voltage is greater than (34.2 - 37.8 ) voltage range