## Slide 1: Vending Machine Hardware Design
A Strawman plan

## Slide 2: Assumptions
We want to pretend small company.
We want to minimize the NRE, Non Recurring Costs
We need to develop systems that can be reused in other projects and have a few years of life span.
We need to get the system out as fast as possible.

## Slide 3: What I believe the motor arrangement is similar to a matrix key board as shown below

## Slide 4: The difference is
The switches are replaced by motors
The rows are high side ( + voltage ) switches which turn on only one row.
The columns are low side (-voltage ) switches which turn on only one column.
This allows only one motor to turn

## Slide 5: To synchronize the motion of the vending action
There is a third pin which appears to pull down for a period of time during the rotation. This is used to synchronize the vending machine operation.
Resistor
Motor 1
Motor 2
Motor …
Motor N
comparator
Microprocessor
Power

## Slide 6: Cable harness and low side switches
For small to medium volumes the fabrication of cable harnesses can be labor intensive to build as well as test.
Low side switches are very cheap, particularly if motor current is .5 amps or below.
  The UNL2303B from TI store in 1’s is $.89
  A Lady Ada favorite part.
My approach is to remove the need for custom cable harnesses

## Slide 7: ULN2003B Layout Notice the fly back diodes for inductive loads

## Slide 8: Vending Machine System
Raspberry Pi
Site Controller
Vending
Machine
Controller
Slave for Row 1
Slave for
Row 2
Slave for
Row n
WIFI Communication
BLE Communication
Slave to
Detect
Vending
Machine
Product
Pickup Bin

## Slide 9: Salient Points
There are two types of cables.
3 wire cables which connect the vending machine controller to the slave nodes
  Wires
    Hi for motor
    Hi for slave
    Common Low
  Separate Hi for motor allows the slave to function if motor shorts
3 wire cable from slave unit to each motor.
  Hi for Motor
  Low for Motor
  Line for synchronization

## Slide 10: Salient Points Continued
BLE was chosen to be communication mechanism within the case because a BLE processor would be as cheap as a processor with a high grade industrial RS485 transceiver.
With the addition of upcoming BLE mesh, the BLE solution may be more attractive.

## Slide 11: Salient Points Continued
Slave Unit
BLE Processor
ESP32 ??
Darlington Pair Low
Drivers
24 to
3.3
Switching
Regulator
Comparator
Sense line from
motors
To motors
Slave would have one command. Spin motor one cycle
Pins to identify Vending Machine Row

## Slide 12: Salient Points Continued
Vending Machine Controller Hardware
24 Volt
To 3.3 Volt Switching
Regulator
ESP32
Processor
High End Driver
PWM Bridge
Current
Sense
Resistors
High Side Motor Drive
Motor Return Current
Measure
Vending
Machine
Motor
Current

## Slide 13: Hardware
Hardware Design consists of assembling modules
  ESP32
  24V – 3.3 DC switching regulator
  Bridge Module
  ULN23003B are in dips and easy to make modules
Main Cost of Hardware will be in plastic enclosures

## Slide 14: Vending Machine Controller Software
Raspberry PI
Redis DB
Vending Machine Controller ESP32
Slave Modules

## Slide 15: Vending Machine Software Steps
Initial Operations
  Open Connection to Redis Data Base and Access Graph Database
  Identify Slaves
  Verify Connections with Slaves
  Open up RPC server to accept commands from Raspberry PI
  Power High Side Motors off
Steady State Operation
  Verify Operation of Slaves
  Verify Product Bin is Closed – Report incidents

## Slide 16: Vending Machine Controller
Vend product request for RPC queue
  Issue endowment to start vend to pi side
  Identify Correct slave.
  Turn on High Side Current
  Start Current Monitoring and Recording
  Tell slave to start motor cycle
  Stop if excessive current is received and report back to pi
  Wait for complete from slave.
  Turn off high side power and close current monitoring
  Wait for customer to pick up product.
  Assemble vend package and send it to the redis data base.
  Report Exceptions to the vend transaction

## Slide 17: PI Site Controller
Pi Site Controller will have two functions.
  Control and Monitoring of Vending Machine
  Customer Transaction and the Management of Mark Coin ( Digital Money)
This presentation will address the 1st topic only.
The PI Site Controller consist of two activities
  Monitor Vending Machines that are on the site.
  Manage the vend request from the financial side of the server.
  Support Service Requests from
    Offsite Cloud Monitors
    Factory Fabrication
    Service Technicians
    Service Workers Filling the vending Machine
    4 levels of users